## Slide 1
Smart Factory Production Performance & OEE Improvement
Fictional client: NexaMotion Components GmbH
88.30%
Overall OEE
30-working-day simulated baseline
ST04
Primary constraint
Assembly & Testing
3.28 mo
Payback
Simulated Phase 1 case
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
1

## Slide 2
Case context and analytical objective
Production line
ST01
CNC Machining
→
ST02
Robot Handling
→
ST03
Quality Inspection
→
ST04
Assembly & Testing
→
ST05
Packaging
Consulting question
Which process losses should management prioritize to improve finished-goods throughput and business performance?
Input | Analytical method | Output
Synthetic production, downtime and maintenance data | OEE, Pareto, bottleneck, root-cause and ROI analysis | Prioritized implementation roadmap
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
2

## Slide 3
Performance baseline
88.30%
OEE
96.39%
Availability
93.21%
Performance
Largest OEE component loss
98.28%
Quality
9.74
MTBF (h)
12.45
MTTR (min)
Chart: 
| Availability | Performance | Quality | OEE
KPI | 96.39 | 93.21 | 98.28 | 88.3
• Plant-level performance loss is larger than availability or quality loss.
• Station-level diagnosis is required before selecting improvements.
• The analysis separates downtime problems from true line constraints.
Baseline interpretation
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
3

## Slide 4
Loss diagnosis by station
Chart: 
| CNC | Robot | Inspection | Assembly | Packaging
OEE | 89 | 88.31 | 88.06 | 85.46 | 90.6
Station | Primary loss | Evidence
ST02 Robot Handling | Availability / reliability | Highest downtime: 1,993.35 min
ST03 Quality Inspection | Quality | Lowest quality: 96.81%
ST04 Assembly & Testing | Performance / throughput | Lowest OEE: 85.46%
Main insight
The station with the most downtime is not automatically the bottleneck. ST04 constrains throughput despite ST02 generating the most downtime.
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
4

## Slide 5
Bottleneck and root-cause indicators
97.78%
Line constraint share
ST04 constrained nearly all observed shifts
C
Slowest shift
80.58 sec mean ST04 cycle
ACT-300
Slowest product
82.23 sec mean ST04 cycle
439.6 min
Top ST04 downtime cause
Functional Test Failure
Evidence-based root-cause direction
• Investigate element-level work content and cycle variation at ST04.
• Compare Shift C work sequence, support availability and standard work adherence.
• Analyze ACT-300 assembly/test sequence before adding new capacity.
• Review functional-test failures as a separate availability loss within ST04.
Chart: 
| Assembly & Testing | Other stations
Constraint Shifts | 88 | 2
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
5

## Slide 6
Reliability quick win: ST02 Part Presence Sensor
49
Events
30-working-day period
635.46 min
Downtime
10.59 hours
33.07%
Share of ST02 unplanned
One failure mode
12.97 min
Average event
Frequency + recovery problem
Interpretation
The sensor issue is a concentrated reliability loss. However, the business case shows no immediate finished-output gain while ST04 remains the active constraint.
Improvement lever | Purpose
Sensor inspection and mounting check | Reduce recurrence
PLC diagnostics / alarm clarity | Shorten fault identification
Standard recovery procedure | Reduce recovery duration
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
6

## Slide 7
Recommendation and business case
Phase | Action | Reason
1 | ST04 work-element study + standard work | Directly targets active throughput constraint
2 | ST04 functional-test / fixture validation | Addresses cycle and failure losses after initial evidence
3 | ST02 sensor reliability program | Protects newly released capacity and stabilizes robot handling
Simulated Phase 1 business case
€15k
Implementation cost
€54.8k
Year-1 benefit
265%
ROI
3.28 mo
Payback
Final recommendation
Prioritize ST04 throughput improvement first. Treat ST02 as the next reliability workstream after ST04 capacity is released. All financial values are simulated portfolio assumptions.
Synthetic portfolio case | Smart Factory Production Performance & OEE Improvement
7